## Slide 1: 2ⁿᵈ Meeting

## Slide 2: DL End-to-End with cGAN
The paper : https://arxiv.org/pdf/1903.02551.pdf
Replacing the channel with cGAN
The conditioning information is the encoded signal from the transmitter + pilot signal to estimate the channel.
Map N bits to K bits (s-<x) where k<N to reduce dimensionality then send x through channel (x-<y) then y is decoded at the receiver (y-<s^)
Cross-Entropy is the loss function (s – s^)

## Slide 3: DL End-to-End with cGAN
Training each component (transmitter – channel – receiver) separately while others fixed.
Objective is to minimize E2E loss function for (transmitter – receiver) and min-max optimization between G and D for the channel (cGAN).
Training receiver is easy as the loss function is computed there but for training transmitter the cGAN is used for back propagation to compute loss function for transmitter using SGD.
Training channel is to reach the min-max optimization point taking real data from the transmitter and fake data from the generator

## Slide 4: DL End-to-End with cGAN
Results:
AWGN channel using FNN for small blocks → similar performance to Hamming with MLD
AWGN channel using CNN for large blocks → similar to RSC for low SNR - outperform in high SNR
Rayleigh channel using CNN for 64-bit blocks → similar to QAM with RSC
Freq-sel channel vs 64 subcarrier OFDM using 64-bit blocks → outperform OFDM for SNR>7db

## Slide 5: Two Application of DL in physical layer
The paper : https://arxiv.org/pdf/2001.03350.pdf
Signal detection using DL at the receiver considering AWGN channel failed.
It generated asymmetric shape (the constellation points shape).
The optimal algorithm was know so DL can’t outperform.
The shape was wrong due to overfitting with many points which make it easy to use any boundary line to separate between areas.
Approximately, all points where in close small square (area of reception) so outside it there was a random behavior.

## Slide 6: Two Application of DL in physical layer
Algorithm Approximation:
We can approximate an algorithm by training a neural network to produce same results with less complexity.
Training iteratively update the parameter values to reduce approximation error (y-y^).
There are non-linear signal detection (convex– non-convex) both are time-consuming.
We can use deep unfolding to make each layer mimic an iterative of the algorithm which will reduce complexity and solve design problems.

## Slide 7: Two Application of DL in physical layer
Invert unknown functions:
Non-linear distortions occur between transmitter and receiver some of which have unknown functions which can’t be appropriately modeled and estimated.
The offline learning will take y as an input to function g (x=g(y)) then input x to a NN producing y^ so the loss function (y-y^) will be trained to be minimum.
Online learning can be used to deal with the time-varying problems.